## Slide 1
IMMUNOPHENOTYPING OF HEMATOPOIETIC PROGENITOR CELLS BY MULTIPARAMETER FLOW CYTOMETRY

## Slide 2
PROTOCOLS FOR CD34 COUNT
Main Features
Mulhouse All cells acquired, FSC vs SSC and SSC vs CD34
Milan All cells acquired, FSC vs SSC and SSC vs CD34
Nordic All cells acquired, FSC vs SSC and SSC vs CD34
ISHAGE CD45+ cells acquired,
CD45 vs SSC, CD34 vs SSC, CD45 vs SSC, FSC vs SSC
ProCount CD34 bright cells acquired,
DNA vs SSC, CD45 vs SSC, DNA vs CD34

## Slide 3
ISHAGE PROTOCOL
CD45
SSC
R1
CD34
SSC
R2
CD45
SSC
FSC
SSC
R3
R4
gated on R1 and R2
gated on R1 and R2 and R3
gated on R1
Notes: In this method for obtaining the CD34 count, CD45+ events in R1 are acquired. It is assumed that CD45- events represent erythroid cells, platelets and debris, thereby producing a false denominator. For obtaining the count, a region, R2, is drawn around CD34 bright events. This is further restricted to CD45 dim, low side scatter events in R3. Finally, FSC vs SSC is displayed and R4 is drawn to include only the band of cells exhibiting heterogeneous size and low side scatter.

## Slide 4
SSC
CD34
R2
SSC
FSC
MILAN PROTOCOL
R1
Notes: In this protocol SSC vs CD34 and SSC vs FSC is displayed. An acquisition gate, R1, that includes all leukocytes, but excludes dead cells and debris is drawn. The count R2, of CD34 bright cells, is then directly obtained.

## Slide 5
RPCI PROTOCOL
SSC
CD34
R1
R2
gated on
R1 OR R2
FSC
SSC
CD45
SSC
gated on
R1 AND R2 AND R3
R4
R5
R6
R3
SSC
CD34
R1
R2
FSC
SSC
CD45
SSC
R4
R5
R6
R3
Notes: In this protocol, all events are acquired. A region R1, is drawn around CD34 bright cells like both ISHAGE and Nordic protocols. In addition, a second region, R2 is drawn to include CD34 dim events. R3 is drawn, like that in the ISHAGE protocol, to exclude dead cells and debris. Region 4 (CD45-), R5 (CD45 dim) and R6 (CD45 bright) are drawn. In the top row, most CD34+ cells are in the bright cluster (red). Some are differentiating (blue) and losing CD34. Most cells are also CD45 dim. In the bottom row, nearly all the CD34+ cells exhibit dim fluorescence (blue), even though, their FSC vs SSC pattern is identical to those in the top row. Most of these cells are CD45 bright. Both CD45 negative and CD45 bright would be excluded from the count using the ISHAGE protocol. Any CD34 dim cells would be excluded by both the ISHAGE and Nordic protocols.

## Slide 6
SIDE SCATTER
FORWARD SCATTER
R1
R1
Notes: ACQUIRING DATA FOR CD34 COUNT
1. Perform appropriate QC on cytometer to verify its performance.
2. Display FCS vs SSC. Set the FSC threshold just to the left of the microspheres as shown in the figure.
3. Draw a region, R1, beginning on the left side of the beads, changing the angle to exclude the debris, down to end along the x axis then along the right side, up to the top and back to meet the beginning. Because the threshold is lower than the threshold normally used to collect blood cells, it is necessary to provide the live gate (shown as R1 in the figure) so the acquired file does not contain a high frequency of undesired events but includes all the cells and the beads. Collect at least 20,000 events or the amount of sample to get a minimum of 100 CD34+ events, i.e. if <100 CD34+ events, when count = 20,000 continue collection until CD34+ = 100 events or collect the entire specimen.
Note: You can not analyze data not acquired!

## Slide 7
Notes: Getting the Correct CD34 HPC Count
1. Display SSC vs CD34, FSC vs SSC and CD45 vs CD14 .
2. Establish a region (R1) to include all CD34+ cells (red) and a region (R2) to include CD14+ cells (green) in the CD45 vs CD14 view. Also draw R4 around the beads (dark blue) and R5 around the lymphocytes (cyan).
3. Using lymphocytes as a landmark in the first view, adjust the sides of R1 to line up with them. Using monocytes as a landmark, put the bottom of R1 on top of them.
4. In the ungated FSC vs SSC view, draw the region R3 to include all lymphocytes, including those under the monocyte population. Gate the second FSC vs SSC on R1 to see the CD34 events inside R3. Determine the percentage CD34+ hematopoietic progenitor cells (HPCs) using the gate “R1 and R3”. Also determine the number of beads counted in R4.
5. Calculate the absolute number of CD34+ HPCs in the sample analyzed as:CD34 HPC/ml = (R1 and R3 count) (number of beads added) ÷ (R4 count) (sample volume)(237 x 109,200) ÷ (3,668 x 0.4 ml) = 17,639

## Slide 8
SSC
CD34
MOSTLY BRIGHT AVERAGE BRIGHT MOSTLY DIM
Notes: Expression of CD34 by Hematopoietic Progenitor Cells. As progenitor cells differentiate into mature cells, they lose CD34. This produces patterns, when SSC vs CD34 is plotted, similar to a rain storm: the cloud, represented by immature CD34 brightly stained cells, and the falling rain, represented by the differentiating cells. As shown on the left, a high frequency of cells are CD34 bright, in the middle view, both CD34 bright and dim cells are found, and on the right, mostly dim cells.

## Slide 9
Comparison of Gating Strategies
%CD34 positive*
        RPCI 1.33 ± 1.44
        ISHAGE 0.87 ± 1.30
        ISHAGE (no CD45 gate) 1.35 ± 1.44
        *n = 80

## Slide 10
What CD34 Count is Important?
Protocol to Use
  Pre or Post Thaw Count? Any
  CD34 bright? or CD34 dim? RPCI
  CD45+? CD45-? Any, except ISHAGE
Notes: Obtaining the CD34 count on hematopoietic products for transplant is an important quality assurance procedure. Multi-institutional studies show that both the Nordic (or Milan) and ISHAGE protocols provide reproducible results indicating a high degree of precision. We showed, however, that they may not be accurate. Thus, each laboratory reproducibly obtains the same wrong result. But it may not matter. As long as the count represents a serogate of the true result, the process still provides the desired quality assurance when the particular protocol is uniformly followed. What may be more important is the quality of the actual product being infused. Here, there is a paucity of data.

## Slide 11
CD34
SSC
CD14
CD45
threshold
Notes: Acquiring CD34+ Subsets
For CD34 subset analysis, we recommend using a CD34 trigger. This strategy provides for the collection of several hundreds of CD34+ cells while not filling a file with thousands of undesired events. To set the CD34 acquisition threshold, refer to the figure. 1) In the left view, CD45 vs CD14, draw a region R2 around the monocytes and activate this region to color the monocytes in SSC vs CD34. 2) Set the PE threshold, shown in the right view, SSC vs CD34, at the top boundary of the CD14+ cluster to acquire some of these along with CD34+ cells. 3) For all tubes stained with the antibody combinations, shown in the Table of antibody combinations, collect a minimum of 2000 events or all of the sample.

## Slide 13
GATED ON R1
GATED
ON
R1 AND R3
SSC
CD14
GATED ON R2
CD45
R4
R5
R9
R6
R7
R8
R4
R5
R9
R6
R7
R8
R10
R11
R15
R12
R13
R14
SSC
FSC
CD45
FSC
GATED
ON
R2 AND R3
CD14
R3
R3
R3
UNGATED
R1
R2
CD34
FSC
Notes: For the determination of CD34 HPC subsets, the antibody combinations shown in the Table were used. Because we wanted to compare our gating strategy with that recommended by ISHAGE, we evaluated six subsets of CD34+ cells, shown in the figure.
1. Draw a region R2 inside R1 to extend from the bottom of R1 to the bottom of the CD34 bright cluster.
2. Display CD45 vs CD14 and gate it on R3 as described above for obtaining the HPC count.
3. Apply quadrant markers R4 - R7. Using the bright cluster of lymphocytes, draw R8 and R9 to evaluate CD45 bright CD14- and + cells respectively.
4. Now gate the FSC vs SSC display on R1 and the CD45 vs CD14 display on “R1 and R3”. This provides an evaluation of the expression of CD45 and CD14 on all the CD34+ cells.
5. To obtain the CD34 dim cells, display FSC vs SSC gated on R2 and CD45 vs CD14, gated on “R2 and R3”.
6. Copy regions R4 - R9 into this display as R10 - R15. This provides an evaluation of the expression of CD45 and CD14 on CD34 dim cells.
7. To obtain the frequency of CD34 bright cells subtract the subset value of CD34 dim from the total CD34.
Files containing the data of the other subset antibodies are then analyzed using this template.

## Slide 14
FREQUENCY OF PATIENTS EXPRESSING CD34 BRIGHT HPCs
CD34 BRIGHT (%TOTAL CD34+ HPCs)
PERCENT OF PATIENTS
Notes: The frequency distribution of CD34 bright as a percentage of total CD34+ HPCs is shown. Only 1/3 of CD34 HPCs are bright in PBSC specimens most frequently encountered.

## Slide 15
CD45 EXPRESSION ON HPCs
PERCENT
Notes: HPCs can be divided into six subsets based on CD45 expression as shown in this figure. There is nearly the same fraction of CD45 B-cells in both the CD34B and CD34D subsets. While the frequency of CD45N and CD45B is the same for CD34B, there is a higher frequency of CD45N among the CD34D subsets. This is consistent with the view that as erythroid and megakaryocytic HPCs differentiate they lose both CD45 and CD34. This hypothesis cannot be proven nor denied if one never acquires the data.

## Slide 16
Notes: Subsets of CD34 progenitor cells are shown from left to right. T-progenitor cells (CD5+) are not found in the bone marrow but the two B-progenitor cell populations, CD19+CD5+ and CD19+CD5- are. Megakaryocyte progenitor cells are resolved using CD41, while activated progenitor cells are CD71+. CD33 with heterogeneous expression of CD4 is found on myeloid progenitor cells. Finally multipotent stem cells are presumed to be CD38 and HLADr negative.

## Slide 17
Proportion of Subset in CD34+ Population
% of Subset in CD34+ Population
0
20
40
60
80
100
CD38
HLADr
-/-
-/+
+/-
+/+
-/-
-/+
+/-
CD45RO
CD45RA
+/+
Notes: These two antibody combinations do not resolve specific subsets, but the most mature HPCs are CD38+HLADr+ and represent about 60% of the total.

## Slide 18
Proportion of Subset Cells in CD34+ Population
% of Subset CD34+
Notes: The lineage differentiation commitment of HPCs can be determined using specific combinations of antibodies to mature hematopoietic cells. CD56 is expressed on a subset of monocytes and on NK cells and 40% of their progenitor cells also coexpress CD15. There are two populations of B-cell progenitors, the most frequent population expresses CD19 but not CD5, the second population expresses both CD19 and CD5. Myeloid progenitor cells can be resolved using CD33 and CD4. Erythroid progenitor cells can be resolved from other activated HPCs by evaluating the CD71+CD45- fraction. CD71 expression on this fraction is very bright. Similarly, megakaryocytes are resolved by evaluating the CD41+CD45- fraction. Because platelets bind to HPCs, interpretation of their frequency can be artifactual.

## Slide 19
Measurement of CD34 Subset Proliferation
Hoechst
Hoechst
Hoechst
Hoechst
number
number
number
number
HLADr
TC
CD38 FITC
Notes: Viable cells can be stained with the vital dye Hoechst 33342 and stained with specific antibodies to resolve the proliferative status of defined subsets. In this example, CD34+ cells are collected with a CD34 trigger. After gating on R1 and R3, the bivariate display of CD38 vs HLADr is used to visualize the subsets defined by the quadrant markers. The DNA distribution of cells in each quadrant is then viewed.

## Slide 20
C-KIT RECEPTOR EXPRESSION ON HPC SUBSETS
CD117
H
L
A
D
r
CD117
CD117
CD117
CD38
Notes: We usually evaluate cell subsets using antibodies to differentiation antigens. Now we can also determine cellular function at the same time. In this example, HPC subsets expressing the cytokine receptor to c-kit is shown.