## Slide 1: BMS 631 - Lecture 2 - Who’s and Why’s of Flow Cytometry
Who’s and Why’s of Flow Cytometry
The History of Flow Cytometry:
An introduction to the early beginnings of flow cytometers; the rationale for early investigations; a summary of the state-of-the-art; the events that led to modern cytometry; early fluorescent dyes; image analysis; DNA cytology
Reading materials: (Shapiro 3rd ed. Pp 43-71; 4th Ed. Shapiro pp 73-100)
All materials used in this course are available for download on the web at http://tinyurl.com/2wkpp
Lecture last modified Jan, 2024
J. Paul Robinson, PhD
Distinguished Professor of Cytometry
Professor of Biomedical Engineering
Notice: The materials in this presentation are copyrighted materials. If you want to use any of these slides, you may do so if you credit each slide with the author’s name. It is illegal to place these notes on CourseHero or any other site.

## Slide 2: Learning Objectives
At the conclusion of this lecture you should understand:
Important historical contributions to the development of flow technology
The driving force for instrument development
Basic concepts used in flow cytometry
Let’s go back over 50 years

## Slide 3: Dittrich & Göhde
Dittrich & Gohde - 1969 - Impulscytophotometer (ICP)- used ethidium bromide for a DNA stain and a high NA objective used as a condenser and collection lens
Laerum, Göhde, Darzynkiewicz (1998)
Photos ©2000 – J.P. Robinson
Göhde and Laerum (1998)

## Slide 4: More on Wolfgang Göhde
Flow Cytometry Pioneer – First fluorescence commercial flow cytometer
Established a flow cytometry company in Germany (Partec) and was responsible for bringing lower cost instruments to Africa and other resource limited countries.

## Slide 5: History
Phywe AG of Gottingen (1969) - produced a commercial version of the ICP built around a Zeiss fluorescent microscope
http://www.partec.de/partec/flowmuseum.html
ICP 11 (1969)
Distributed by Phywe, Göttingen
The first commercial flow cytometer
PDP 11 computer
Wolfgang Göhde discussing his work in Africa in 2007
Video 54 s

## Slide 6: Pre 1969 – Fulwyler, van Dilla etc. we have discussed
Len Herzenberg - 1969 - sorter based on fluorescence (arc lamp) built after working with one of Kamentsky’s RCS systems where they built an instrument they called the Fluorescence Activated Cell Sorter (FACS)
Photos from 2000 – J.P. Robinson
Herzenberg

## Slide 7: Herzenberg & Becton-Dickinson
Herzenberg -1972- Argon laser flow sorter - placed an argon laser onto their sorter and successfully did high speed sorting - Coined the term Fluorescence Activated Cell Sorting (FACS) This instrument could detect weak fluorescence with rhodamine and fluorescein tagged antibodies. A commercial version was distributed by B-D in 1974 and could collect forward scatter and fluorescence above 530 nm.
Herzenberg was the recipient of the very
Prestigious 2006 Kyoto Prize for his work
in development of fluorescence based
flow cytometry. Many people well known
in the field were trained in his lab
(Photo from the official Kyoto Prize website)

## Slide 8: The driving force for Len Herzenberg
Video 2:05
Reproduced with Permission
Smithsonian

## Slide 9: Why sorting and Fluorescence?
Video 5:17
Reproduced with Permission
Smithsonian

## Slide 10: Kamentsky
Kamentsky - Bio/Physics Systems - 1970 commercial cytometer - the “Cytograph” He-Ne laser system at 633 nm for scatter (and extinction) - supposedly the first commercial instrument incorporating a laser. It could separate live and dead cells by uptake of Trypan blue. A fluorescence version called the “Cytofluorograph” followed using an air-cooled argon laser at 488 nm excitation
1970 Cytograph presently at the Purdue University Cytometry Laboratories
Photo ©2000 – J.P. Robinson
This is an example of
an early commercial
instrument that measured
scatter using a laser

## Slide 11: First Ultraviolet Imaging
A. Kohler, Mikrophotographische Untersuchungen mit ultraviolettem Licht, Z. Wiss. Mikroskopie 21, 1904
A. Kohler 1904
Salamander maculosa larva epidermal cells - 1300 X
275 nm
280 nm
Dr. Kamentsky

## Slide 12: Feulgen Reaction 1924
R. Feulgen & H. Rossenback, Microskopisch-chemischer Nachweis einer Nucleinsaure von
Typus der Thymonucleinsaure und auf die darauf berunhende elektive Farbung von
Zellkernen in mikroskopischen Präparaten, Hoppe Seyler Z. Physiol. Chem. 135, 1924
Schema of formation of Schiff Reagent from Pararosanilin and its reaction with aldehydes to form colored products
After Wieland and Scheuing (1921)
Shortened from Kasten (1960)

## Slide 13: UV Measurements of DNA and Cytoplasm
Uber den chemischen Aufbau der Strukturen des Zellkernes, Skand. Arch. Physiol. 73, 1936
Ultraviolet absorption measurements of
a grasshopper metaphase chromosome
Densitometer traces across
a region of the chromosome
Cytoplasmic absorption
Background signal
Extinction values for chromosome and cytoplasm plotted against wavelength
T. Caspersson 1936
Chromosomal absorption

## Slide 14: Relating Cytometry to Pathology O. Caspersson 1964
Quantitative cytochemical studies on normal, malignant, premalignant and atypical cell populations from the human uterine cervix, Acta Cytologica 8, 1964
(ref 49068)
Frequency distribution of DNA content
Cells from a normal cervix
Cells from a cervical carcinoma
Premalignant cells from the epithelium

## Slide 15: Early Microfluorometric Scanner Robert Mellors 1951
RC Mellors & R. Silver, A microfluorometric scanner for the differential detection of cells: application to exfoliative cytology, Science 104, 1951
Fluorescence photomicrograph
Phase photomicrograph
Voltage trace

## Slide 16: Cytometry Analytic Techniques M.R. Mendelsohn 1958
The Two-Wavelength Method of Microspectrophotometry
J. Biophys. Biochem Cytol. 4, 1958

## Slide 17: Flow Cell Counter - First Try Andrew Moldavan 1934
Refman: 4478

## Slide 18: Two-Color Cell Counter Patent JC Parker and WR Horst 1953

## Slide 19: Sheath Flow PJ Crosland-Taylor 1953
A device for counting small particles suspended in fluid through a tube, Nature 171, 1953 (ref 4756)
An Electronic Blood-Cell Counting Machine, Blood 13, 1958 (ref 40974)

## Slide 20: Coulter Counter 1956

## Slide 21: Before Cytometry
LA Kamentsky & CN Liu, Computer-automated design of multifont print recognition
logic, IBM J. Research & Development 7, 1963 (ref 40705)
Dr. Kamentsky

## Slide 22: Kamenstsky’s work at IBM and Character recognition
Video 1:17

## Slide 23: Kamenstky explains how IBM became involved with pathology
Video 1:12

## Slide 24: Visible & UV Scanning
Brightfield Image
UV Images
Dr. Melamed
Dr. Koss
Dr. Kamentsky

## Slide 25: UV Scanning Measurements
Ultraviolet Absorption in Epidermoid Cancer Cells LA Kamentsky, H. Derman,
and MR Melamed, Science 142, 1963 (ref 40210)
Normal Cells
Cancer Cells
Dr. Kamentsky

## Slide 26: Flow Cytometry
LA Kamentsky, MR Melamed & H. Derman, Spectrophotometer: New instrument for ultrarapid cell analysis, Science 150, 1965 (ref: 4144)

## Slide 27: Flow Cytometry
LA Kamentsky, MR Melamed & H. Derman, Spectrophotometer: New instrument for ultrarapid cell analysis, Science 150, 1965 (ref: 4144)

## Slide 28
Epidermoid carcinoma
at pH 2.1
Normal colonic epithelium
Epidermoid carcinoma
of the cervix
Epidermoid carcinoma
at pH 3.8
Normal epidermoid
epithelium
Flow Cytometry

## Slide 29
Kamensky gives up on imaging and starts flow cytometry - 1963
Video 1:42

## Slide 30: First Analytic Flow Instrument 1963

## Slide 31: More Sensors and Sorting 1965
Spectrophotometric Cell Sorter, LA Kamentsky and MR Melamed, Science 156, 1967 (ref 4134)
Slide Kindly Supplied by Compucyte

## Slide 32: More Sensors and Sorting 1965
Spectrophotometric Cell Sorter, LA Kamentsky and MR Melamed, Science 156, 1967 (ref 4134)

## Slide 33: Four Sensors, Sorting, Auto Sampling and Computer Data Reduction 1966
Two analytic instruments were built and one was delivered to LA Herzenberg at Stanford University 1967

## Slide 34: Evolution of Flow Instruments
WA Bonner, HR Hulett, RG Sweet and LA Herzenberg,
Fluorescence Activated Cell Sorting, Review of Scientific Instruments 43, 1972

## Slide 35: Electrostatic Printing and Droplet Sorting RG Sweet - MJ Fulwyler
RG Sweet, Fluid Droplet Recorder
U.S. Patent 3,596,275
filed 3/25/64 (ref 40975)
MJ Fulwyler, Particle Separator, U.S.
Patent 3,380,584 filed 6/4/65

## Slide 36: Impulsecytophotometer W. Dittrich and W. Gohde 1969
W. Dittrich and W. Gohde, Impulsfluorometrie bei Einzelzellen in Suspensionen,
Zeit. F Naturforschung 24b, 1969 (ref 4755)

## Slide 37: Los Alamos Contributions
MA VanDilla, TT Trujillo, PF Mullaney &
JR Coulter, Cell Microfluorometry: A
Method for Rapid Fluorescence Measurement,
Science 163, 1969
PM Kraemer, DF Petersen & MA Van Dilla, DNA Constancy in Heteroploidy and the Stem
Line Theory of Tumors, Science 174, 1971

## Slide 38: Evolution of Leukocyte Gating Strategy for Cluster Subsetting
GC Salzman, JM Crowell,
JC Martin, TT Trujillo,
A. Romero, PF Mullaney, & PM LaBauve, Cell classification by laser light scattering: identification and separation of unstained leukocytes,
Acta Cytologica 19, 1975
LR Adams & LA Kamentsky,
Machine characterization of human leukocytes by acridine orange fluorescence, Acta Cytologica 15, 1971
RA Hoffman, PC Kung,
WP Hansen, Simple & rapid
measurement of human T
lymphocytes and their
subclasses, PNAS 77, 1980
Lymphocytes
Monocytes
Granulocytes

## Slide 39
Biophysics Systems
Ortho Instruments
Cytograf (1970)
Cytofluorograf (1970)
FC200 (1975)
ELT 8 (1977)
50H (1978)
Spectrum (1979)

## Slide 40: Mack Fulwyler
Coulter Electronics manufactured the TPS-1 (Two parameter sorter) in 1975 which could measure forward scatter and fluorescence using a 35mW argon laser.
This photo (left) (©2000 – J.P. Robinson) is one of only one or two surviving TPS Instruments. It is very similar to the Coulter Counter of the day.
Photo ©2000 – J.P. Robinson

## Slide 41: Shapiro (sadly passed away in Nov, 2021)
Shapiro and the Block instruments (1973-76) - a series of multibeam flow cytometers that did differentials and multiple fluorescence excitation and emission
Photos ©2000 – J.P. Robinson

## Slide 42: Hemalog D
Technicon - Hemalog D - 1974 - first commercial differential flow cytometer - light scatter and absorption at different wavelengths - chromogenic enzyme substrates were used to identify neutrophils and eosinophils by peroxidase and monocytes by esterase, basophils were identified by the presence of glycosaminoglycans using Alcian Blue - the excitation for all measurements was a tungsten-halogen lamp
Insert photos on page 60
Image from Shapiro “Practical Flow Cytometry”, 3rd. Ed.Wiley-Liss, 1994

## Slide 43: Monoclonal Antibodies
Georges J.F. Köhler The Nobel Prize in Physiology or Medicine 1984
Born: 17 April 1946, Munich, Germany
Died: 1 March 1995, Freiburg im Breisgau, Germany
César Milstein was awarded the 1984 Nobel Prize in Physiology or Medicine jointly with his former postdoctoral fellow Georges J. F. Köhler (AAI '85) and theoretician Niels Jerne (AAI '73). Milstein and Köhler won the prize for developing the hybridoma method of producing monoclonal antibodies.
Published in a letter to Nature (I understand that the paper was not accepted originally as a full paper so they submitted it as a letter)

## Slide 44: Monoclonal Antibodies 1975
Kohler and Milstein's hybridoma technology (1975)
Noble Prize in 1984
Video 0.40
Video from Novelprize.org
Newsreel from the day the Nobel Prize was announced

## Slide 45: Coulter Electronics
1977-78 developed the Epics series of instruments which were essentially 5 watt argon ion laser instruments, complete with a multiparameter data analysis system, floppy drive and graphics printer.
Epics V front end (left) and MDADS (right)
Photos ©2000 – J.P. Robinson
Huge computer
racks all with
oscilloscopes

## Slide 46: Biophysics -Ortho
Ortho Diagnostics (Johnson and Johnson) purchased Biophysics in 1976 and in 1977 the System 50 Cytofluorograph was developed - this was a droplet sorter, with a flat sided flow cell, forward and orthogonal scatter, extinction, 2 fluorescence parameters, multibeam excitation, computer analysis option.
1979 - NIH scientists had added a krypton laser at 568 nm to excite Texas Red fluorescence at 568 nm and emit at 590-630 nm. Argon (488 nm FITC was measured simultaneously without signal cross-talk - thus the FACS IV was developed (B-D).
FC 200(1975)
System 50H (1978)

## Slide 47: Stuart Schlossman
Schlossman at the Farber Institute in Boston, began to make monoclonal antibodies to white blood cell antigens in 1978. Eventually he collaborated with Ortho Diagnostics who distributed the famous “OK T4” etc., Mabs
BD as well as Coulter Immunology also distributed his antibodies, and this resulted in some interesting legal issues in the late 1980’s and early 1990’s
Monoclonal Antibodies:
Kohler G, Milstein C. Continuous cultures of fused cells secreting antibody of predefined specificity. Nature Lon. 1975;256:495-497.
Monoclonal antibodies defining distinctive human T cell surface antigens
P Kung, G Goldstein, EL Reinherz and SF Schlossman Science 19 October 1979: Vol. 206 no. 4416 pp. 347-349 DOI: 10.1126/science.314668

## Slide 48: Introductory Terms and Concepts
Variable/Parameter (see Note below)
Light Scatter- Forward (FALS), narrow (FS)
- Side scatter, Wide angle, 90 deg, Orthogonal
Fluorescence – band width, or spectral range
Absorption/axial light loss
Time
Count
Note: People in the field of flow cytometry interchangeably use the term “parameter”
with “variable”. While it is technically incorrect to use the term parameter unless we are
talking about a derived value, it is common usage.

## Slide 49: Concepts
    Scatter: Size, shape, granularity, polarized scatter (birefringence), effective refractive Index
    Fluorescence:
    Intrinsic: Endogenous pyridines and flavins
    Extrinsic: All other fluorescence profiles
    Absorption
    Axial Light loss: Loss of light (blocked) (best measure for particle size)
    Time: Useful for kinetics, Quality Control, stop count
    Cell Count: Always part of any collection
    Tube Number or Identifier /well number

## Slide 50: Instrument Components
Electronics: System control, pulse collection, pulse analysis, triggering, time delay, data display, gating, sort control, light and detector control
Optics: Light source(s), detectors, optical filters, spectral separation
Fluidics: Specimen control, sorting, rate of data collection
Computation/Data Analysis: Data display & analysis, multivariate/ simultaneous solutions, identification of sort populations, quantitation, ratios

## Slide 51: Data Analysis Concepts
    Data plotting
    Single parameter - Histogram
    Dual parameter – Dot plot
    Multiple parameter – 3 D plot or a variety of plots such as PCA* or other analytical displays
    Complex plots – time course, concentration curves, cell cycle analysis, heat maps, plate maps, etc.
    tSNE, UMAP, and a variety of displays are currently used in flow cytometry
Note: these terms are introduced here, but will be discussed in more detail in later lectures
* PCA – Principal Component Analysis

## Slide 52: Data Presentation Formats
    Histogram
    Dot plot
    Contour plot
    3D plots
    Dot plot with projection
    Overviews/composites (multiple histograms)
    Various analytical plots
    Complex analysis like SPADE, tSNE, UMAP, PCA
How flow cytometry data are presented: Examples
0
200
400
600
800
1000
Side Scatter Projection
Forward Scatter Projection
90 Degree Scatter
Neutrophils
Lymphocytes
Monocytes
Forward Scatter
Thanks Wiki
From OIMP-069

## Slide 53: Data Analysis Concepts
    Gating
    Single parameter
    Dual parameter
    Multiple parameter
    Back gating
Note: terms are introduced, but will be discussed in more detail in later lectures
Gating is a fundamental part of flow cytometry data collection & Analysis
Gate
Gate
Linear Gate
2P Gate
What do you analyze and what do you ignore?
For example
You can evaluate these cells
and ignore
these

## Slide 54: Sorting
Sorting is the process of physically separating a cell from a population
Sorting can be accomplished by a number of techniques, but the primary one is electrostatic sorting (microfluidic chips are also effective)
Sorting can be 1-way, 2-way, 4-way or 7-way in modern sorters
Sorting can be accomplished under sterile conditions for subsequent cell culture
Sorting can be achieved at high speeds over 100,000 events per second
Newest sorters include SPECTRAL sorters that can use spectral unmixing to sort (e.g. Thermo Bigfoot)

## Slide 55: Lecture Summary
History of Flow Cytometry
Some Key Individuals
Key ideas that established current approaches
Introduction to terms of use in flow cytometry